## Slide 1
⚡
Smart Meter System Logic
BY Cohort-6
Data validation, circuit logic, threshold logic and communication

## Slide 2
Data validation
Why validation matters
Input checks
Voltage is constrained to 220-240 V in the simulator so the demo stays inside a realistic domestic supply range for the project.
Device states
Fan, bulb and TV states are validated as ON/OFF inputs before assigning current values, preventing invalid appliance combinations.
Range filtering
Current values can be fixed or randomized inside safe ranges, such as fan current varying from 0.09 A to 0.43 A for realistic simulation.
Formatted serial data
LabVIEW sends clean comma-separated values in the form voltage,current so the ESP32 can parse the packet reliably every cycle.

## Slide 3
Data validation
Validation flow
1
Read controls
Read voltage knob and appliance switches from LabVIEW front panel.
2
Apply ranges
Limit voltage and assign current only when a load is enabled.
3
Build packet
Convert values to %f,%f format and push through VISA Write.
4
Check in ESP32
Parse serial data, reject bad values, then compute total power.

## Slide 4
Circuit logic
Functional circuit path
LabVIEW side
Voltage control acts as the supply source.
Fan, bulb and TV switches represent simulated loads.
Select blocks assign current when each load is ON.
Compound Arithmetic adds all branch currents.
ESP32 side
Serial port receives voltage and total current.
Controller calculates power using P = V x I.
Latest values are stored for dashboard upload.
Cloud update sends a meter-like reading packet.

## Slide 5
Circuit logic
Load model example
🌀
Fan
Variable current can be mapped between 0.09 A and 0.43 A to mimic speed and load fluctuation.
💡
Bulb
A smaller current band can represent steady lighting behavior with slight random variation.
📺
TV
A wider band can simulate real consumption changes based on screen brightness and activity.
Total current = fan current + bulb current + TV current, and total power = voltage × total current.

## Slide 6
Threshold logic
Decision rules
Normal
Power remains in the safe operating band, so the dashboard shows standard green status.
Warning
If total power crosses a preset soft threshold, the system can flag a high-consumption alert.
Critical
If the limit is exceeded again, the system can trigger a critical event, notification or cut-off logic.

## Slide 7
Threshold logic
Suggested thresholds
Voltage rules
Below 220 V: low-voltage condition.
220-240 V: normal operating region.
Above 240 V: over-voltage condition.
Power rules
Below threshold: normal load profile.
Near limit: send warning notification.
Above limit: mark anomaly or overload event.
These thresholds can later support Telegram alerts, dashboard color changes, or relay-based protection logic.

## Slide 8
Communication
End-to-end data flow
🖥️
LabVIEW
Generates validated voltage and load values.
🔌
NI-VISA
Transfers serial packets over USB to the ESP32.
📡
ESP32
Parses, computes and prepares cloud-ready data.
☁️
Dashboard
Displays periodic energy monitoring results every 20sec

## Slide 9
📊
Communication extensions
ThingSpeak
Quick prototype option for periodic visualization and initial cloud testing.
Custom dashboard
Streamlit or HTML, CSS and JS can provide a richer live monitoring interface.